Elmerfem: Quench with circuit
Case study: Superbend
F. Trillaud(1) <ftrillaudp@gmail.com>, E. Takala(2) <eelis.takala@gmail.com>
(1): Instituto de Ingeniería, UNAM, Mexico
(2): Elemental Reality Solutions (ERS), Finland

---
Miscellaneous
1. Ubuntu 20.04LTS
2. Elmerfem 9.0 <http://www.elmerfem.org/blog/>
3. Salome 9.9.0 <https://www.salome-platform.org/>
4. Paraview 5.6 <https://www.paraview.org/>

---
Case study
1. Three closed coils inside an iron yoke.
2. Coil cross-section: 0.05 m x 0.05 m
3. Inner radius: 0.2 m
Magnetic core
Air
Coil 1
Coil 2
Coil 3

---
Meshes
Coil 1 & 3
Coil 2
Magnetic core
Air

---
Groups on meshes
1. Volumes
2. Racetrack coils (1, 2): Ωc1, Ωc2
1. Circular coils (3, 4): Ωc3, Ωc4
2. Magnetic core: Ωmc
1. Air: Ωcc
3. Boundaries
4. Racetrack coils (1, 2): Γc1, Γc2
Circular coils (3, 4): Γc3, Γc4
Air: Γcc
\Omega_{cc}
\Gamma_{cc}
\Omega = \Omega_{c1} \cup \Omega_{c2} \cup \Omega_{c3} \cup \Omega_{c4} \cup \Omega_{mc} \cup \Omega_{cc}
\Omega_{c1,2,3,4}
\Gamma_{c1,2,3,4}

---
Circuit model
Two circuits with a dumping resistor in parallel:
1. Racetrack coils 1 and 2 connected in series
2. Circular coils 3 and 4 connected in series
Circuit 1: racetrack coils 1 & 2
Circuit 2: circular coils 3 & 4

---
Circuit equations
1. Both circuits are identical, we present only the equations for the first circuit
2. Circuit 1
Circuit 1, coil 2
NB: the circuit builder adds additional variables such as voltages
V_{S1} = V_{cl1}+V_{1,1}+V_{1,2}
I_{S1} = I_{1,1}+I_{dp1}
V_{cl1} = R_{cl1} I_{S1}
V_{1,1} + V_{1,2} = V_{dp1}
V_{dp1} = R_{dp1} I_{dp1}
I_{1,1} = I_{1,2}
I_{cl1} = I_{SI}

---
Circuit builder
 1 import sys
 2 from elmer_circuitbuilder import *
 3
 4 def main(argv=None):
 5 output_file = "circuits.definitions_tmp"
 6 # ---------------------------------------------------------------------------
 7 c = number_of_circuits(2)
 8 # ---------------------------------------------------------------------------
 9 c[1].ref_node = 1
10 PS1 = I("IS1", 1, 2, 1.0)
11 Rcl1 = R("Rcl1", 2, 3, 1.0)
12 Rdp1 = R("Rdp1", 3, 1, 1.0)
13 FEM_1 = ElmerComponent("Coil1", 3, 4, 1, ["Coil1"])
14 # FEM_1 = ElmerComponent("Coil1", 3, 4, number of the Component field in sif == 1 associated to coil 1, ["Coil1"])
15 FEM_1.is3D()
16 FEM_1.stranded(1, 0)
17 FEM_1.isClosed()
18 FEM_2 = ElmerComponent("Coil2", 4, 1, 2, ["Coil2"])
19 FEM_2.is3D()
20 FEM_2.stranded(1, 0)
21 FEM_2.isClosed()
22 c[1].components.append([PS1, Rcl1, Rdp1, FEM_1, FEM_2])
23 # ---------------------------------------------------------------------------
24 c[2].ref_node = 1
25 PS2 = I("IS2", 1, 2, 1.0)
26 Rcl2 = R("Rcl2", 2, 3, 1.0)
27 Rdp2 = R("Rdp2", 3, 1, 1.0)
28 FEM_3 = ElmerComponent("Coil3", 3, 4, 3, ["Coil3"])
29 FEM_3.is3D()
30 FEM_3.stranded(1, 0)
31 FEM_3.isClosed()
32 FEM_4 = ElmerComponent("Coil4", 4, 1, 4, ["Coil4"])
33 FEM_4.is3D()
34 FEM_4.stranded(1, 0)
35 FEM_4.isClosed()
36 c[2].components.append([PS2, Rcl2, Rdp2, FEM_3, FEM_4])
37 # ---------------------------------------------------------------------------
38 generate_elmer_circuits(c, output_file)
39 return 0
40
41 if __name__ == "__main__":
42 sys.exit(main() or 0)
1. We used the circuit builder python interface to create the circuit model:
2. https://pypi.org/project/elmer-circuitbuilder/
4. https://github.com/ElmerCSC/elmer-elmag/tree/main/CircuitBuilder
6. We modified by hand the resulting “circuits.definitions_tmp” file. First, we made a copy “circuits.definitions” that is called in the sif file. In this file, we removed the additions to the sif file and the parameters

---
Cicuits.definitions
circuitBuilder.py
Circuits.definitions
 1 ! Matrix Size Declaration and Matrix Initialization
 2 $ C.2.variables = 13
 3 $ C.2.perm = zeros(C.2.variables)
 4 $ C.2.A = zeros(C.2.variables,C.2.variables)
 5 $ C.2.B = zeros(C.2.variables,C.2.variables)
 6
 7 ! Dof/Unknown Vector Definition
 8 $ C.2.name.1 = "i_IS2"
 9 $ C.2.name.2 = "i_Rcl2"
10 $ C.2.name.3 = "i_Rdp2"
11 $ C.2.name.4 = "i_component(3)"
12 $ C.2.name.5 = "i_component(4)"
13 $ C.2.name.6 = "v_IS2"
14 $ C.2.name.7 = "v_Rcl2"
15 $ C.2.name.8 = "v_Rdp2"
16 $ C.2.name.9 = "v_component(3)"
17 $ C.2.name.10 = "v_component(4)"
18 $ C.2.name.11 = "u_2_circuit_2"
19 $ C.2.name.12 = "u_3_circuit_2"
20 $ C.2.name.13 = "u_4_circuit_2"
21
22 ! Source Vector Definition
23 $ C.2.source.12 = "IS2_Source"
24
25 ! KCL Equations
26 $ C.2.B(0,0) = -1
27 $ C.2.B(0,1) = 1
28 $ C.2.B(1,1) = -1
29 $ C.2.B(1,2) = 1
30 $ C.2.B(1,3) = 1
31 $ C.2.B(2,3) = -1
32 $ C.2.B(2,4) = 1
33
34 ! KVL Equations
35 $ C.2.B(3,5) = 1
36 $ C.2.B(3,10) = -1
37 $ C.2.B(4,6) = -1
38 $ C.2.B(4,10) = 1
39 $ C.2.B(4,11) = -1
40 $ C.2.B(5,7) = -1
41 $ C.2.B(5,11) = 1
42 $ C.2.B(6,8) = -1
43 $ C.2.B(6,11) = 1
44 $ C.2.B(6,12) = -1
45 $ C.2.B(7,9) = -1
46 $ C.2.B(7,12) = 1
47
48 ! Component Equations
49 $ C.2.B(10,2) = Rdp2
50 $ C.2.B(10,7) = -1
51 $ C.2.B(11,0) = 1
52 $ C.2.B(12,1) = Rcl2
53 $ C.2.B(12,6) = -1
 1 import sys
 2 from elmer_circuitbuilder import *
 3
 4 def main(argv=None):
 5 output_file = "circuits.definitions_tmp"
 6 # ---------------------------------------------------------------------------
 7 c = number_of_circuits(2)
 8 # ---------------------------------------------------------------------------
 9 c[1].ref_node = 1
10 PS1 = I("IS1", 1, 2, 1.0)
11 Rcl1 = R("Rcl1", 2, 3, 1.0)
12 Rdp1 = R("Rdp1", 3, 1, 1.0)
13 FEM_1 = ElmerComponent("Coil1", 3, 4, 1, ["Coil1"])
14 # FEM_1 = ElmerComponent("Coil1", 3, 4, number of the Component field in sif == 1 associated to coil 1, ["Coil1"])
15 FEM_1.is3D()
16 FEM_1.stranded(1, 0)
17 FEM_1.isClosed()
18 FEM_2 = ElmerComponent("Coil2", 4, 1, 2, ["Coil2"])
19 FEM_2.is3D()
20 FEM_2.stranded(1, 0)
21 FEM_2.isClosed()
22 c[1].components.append([PS1, Rcl1, Rdp1, FEM_1, FEM_2])
23 # ---------------------------------------------------------------------------
24 c[2].ref_node = 1
25 PS2 = I("IS2", 1, 2, 1.0)
26 Rcl2 = R("Rcl2", 2, 3, 1.0)
27 Rdp2 = R("Rdp2", 3, 1, 1.0)
28 FEM_3 = ElmerComponent("Coil3", 3, 4, 3, ["Coil3"])
29 FEM_3.is3D()
30 FEM_3.stranded(1, 0)
31 FEM_3.isClosed()
32 FEM_4 = ElmerComponent("Coil4", 4, 1, 4, ["Coil4"])
33 FEM_4.is3D()
34 FEM_4.stranded(1, 0)
35 FEM_4.isClosed()
36 c[2].components.append([PS2, Rcl2, Rdp2, FEM_3, FEM_4])
37 # ---------------------------------------------------------------------------
38 generate_elmer_circuits(c, output_file)
39 return 0
40
41 if __name__ == "__main__":
42 sys.exit(main() or 0)
1. 1 $ Circuits = 2
2. 2
3. 3 ! Matrix Size Declaration and Matrix Initialization
4. 4 $ C.1.variables = 13
5. 5 $ C.1.perm = zeros(C.1.variables)
6. 6 $ C.1.A = zeros(C.1.variables,C.1.variables)
7. 7 $ C.1.B = zeros(C.1.variables,C.1.variables)
8. 8
9. 9 ! Dof/Unknown Vector Definition
10. 10 $ C.1.name.1 = "i_IS1"
11. 11 $ C.1.name.2 = "i_Rcl1"
12. 12 $ C.1.name.3 = "i_Rdp1"
13. 13 $ C.1.name.4 = "i_component(1)"
14. 14 $ C.1.name.5 = "i_component(2)"
15. 15 $ C.1.name.6 = "v_IS1"
16. 16 $ C.1.name.7 = "v_Rcl1"
17. 17 $ C.1.name.8 = "v_Rdp1"
18. 18 $ C.1.name.9 = "v_component(1)"
19. 19 $ C.1.name.10 = "v_component(2)"
20. 20 $ C.1.name.11 = "u_2_circuit_1"
21. 21 $ C.1.name.12 = "u_3_circuit_1"
22. 22 $ C.1.name.13 = "u_4_circuit_1"
23. 23
24. 24 ! Source Vector Definition
25. 25 $ C.1.source.12 = "IS1_Source"
26. 26
27. 27 ! KCL Equations
28. 28 $ C.1.B(0,0) = -1
29. 29 $ C.1.B(0,1) = 1
30. 30 $ C.1.B(1,1) = -1
31. 31 $ C.1.B(1,2) = 1
32. 32 $ C.1.B(1,3) = 1
33. 33 $ C.1.B(2,3) = -1
34. 34 $ C.1.B(2,4) = 1
35. 35
36. 36 ! KVL Equations
37. 37 $ C.1.B(3,5) = 1
38. 38 $ C.1.B(3,10) = -1
39. 39 $ C.1.B(4,6) = -1
40. 40 $ C.1.B(4,10) = 1
41. 41 $ C.1.B(4,11) = -1
42. 42 $ C.1.B(5,7) = -1
43. 43 $ C.1.B(5,11) = 1
44. 44 $ C.1.B(6,8) = -1
45. 45 $ C.1.B(6,11) = 1
46. 46 $ C.1.B(6,12) = -1
47. 47 $ C.1.B(7,9) = -1
48. 48 $ C.1.B(7,12) = 1
49. 49
50. 50 ! Component Equations
51. 51 $ C.1.B(10,2) = Rdp1
52. 52 $ C.1.B(10,7) = -1
53. 53 $ C.1.B(11,0) = 1
54. 54 $ C.1.B(12,1) = Rcl1
55. 55 $ C.1.B(12,6) = -1

---
Circuit matrix - checked
New variables
To get the large matrix, in preamble of texmath: \setcounter{MaxMatrixCols}{20}
ALL GOOD
A = \begin{pmatrix} -1 & 1 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 \\ 0 & -1 & 1 & 1 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 \\ 0 & 0 & 0 & -1 & 1 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 \\ 0 & 0 & 0 & 0 & 0 & 1 & 0 & 0 & 0 & 0 & -1 & 0 & 0 \\ 0 & 0 & 0 & 0 & 0 & 0 & -1 & 0 & 0 & 0 & 1 & -1 & 0 \\ 0 & 0 & 0 & 0 & 0 & 0 & 0 & -1 & 0 & 0 & 0 & 1 & 0 \\ 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & -1 & 0 & 0 & 1 & -1 \\ 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & -1 & 0 & 0 & 1 \\ 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 \\ 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 \\ 0 & 0 & R_{dp1} & 0 & 0 & 0 & 0 & -1 & 0 & 0 & 0 & 0 & 0 \\ 1 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 & 0 \\ 0 & R_{cl1} & 0 & 0 & 0 & 0 & -1 & 0 & 0 & 0 & 0 & 0 & 0 \end{pmatrix}
\mathbf{b} = \left( 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, IS1, 0 \right)
\mathbf{x} = \left( i_{IS1}, i_{Rcl1}, i_{Rdp1}, i_{component(1)}, i_{component(2)}, v_{IS1}, v_{Rcl1}, v_{Rdp1}, v_{comopnent(1)}, v_{component(2)}, u_{2circuit1}, u_{3circuit1}, u_{4circuit1} \right)
A \mathbf{x} = \mathbf{b}
-i_{IS1} + i_{Rcl1} = 0
-i_{Rcl1} + i_{Rdp1} + i_{component(1)} = 0
-i_{component(1)} + i_{component(2)} = 0
V_{IS1} - U_{2circuit1} = 0
-V_{Rcl1} + U_{2circuit1} -U_{3circuit1} = 0
-V_{Rdp1} + U_{3circuit1} = 0
-V_{component(1)} + U_{3circuit1} -U_{4circuit1} = 0
-V_{component(2)} + U_{4circuit1} = 0
R_{dp1} i_{Rdp1} - V_{Rdp1} = 0
i_{IS1} = IS1
R_{cl1}i_{Rcl1}-V_{Rcl1} = 0

---
Study
1. Non-linear system using B = μ(H)H and σ(T,B)
3. Transient simulation:
1. Charging the magnet
2. Plateau with quench ignition
3. Discharge in external resistor (dumping)
2. Material properties depending on temperature and some cases magnetic field

---
Information
1. Multiphysics problem and implementation: Frederic Trillaud at ftrillaudp@gmail.com
3. FEM coding in Elmerfem, circuit implementation: Eelis Takala at eelis.takala@gmail.com