Elmerfem: multiple circuits
PART I: No dumping scheme
F. Trillaud(1) <ftrillaudp@gmail.com>, E. Takala(2) <eelis.takala@gmail.com>
(1): Instituto de Ingeniería, UNAM, Mexico
(2): Elemental Reality Solutions (ERS), Finland

---
Case study
1. Three closed coils inside an iron yoke.
2. Coil cross-section: 0.05 m x 0.05 m
3. Inner radius: 0.2 m
Magnetic core
Air
Coil 1
Coil 2
Coil 3

---
Meshes
Coil 1 & 3
Coil 2
Magnetic core
Air

---
Groups on meshes
1. Volumes
2. Coils (1, 2, 3): Ωc1, Ωc2, Ωc3
3. Air: Ωcc
5. Boundaries
Coils (1, 2, 3): Γc1, Γc2, Γc3
Air: Γcc
\Omega_{c1,2,3}
\Gamma_{c1,2,3}
\Omega_{cc}
\Gamma_{cc}
\Omega = \Omega_{c1} \cup \Omega_{c2} \cup \Omega_{c3} \cup \Omega_{cc}

---
Circuit model
Two circuits:
1. Coil 1 and 3 connected in series
2. Coil 2 alone
Circuit 1: coil 1 & 3
Circuit 2: coil 2

---
Circuit equations
Circuit 1
Circuit 2
Circuit 1, coil 1
V_{S1} = V_{cl1}+V_{1,1}+V_{1,3}
I_{S1} = I_{1,1}
I_{S1} = I_{1,3}
V_{cl1} = R_{cl1} I_{S1}
V_{S2} = V_{2,2}
I_{S2} = I_{2,2}
V_{cl2} = R_{cl2}I_{S2}

---
Circuit builder
1. We used the circuit builder python interface to create the circuit model:
2. https://pypi.org/project/elmer-circuitbuilder/
4. https://github.com/ElmerCSC/elmer-elmag/tree/main/CircuitBuilder
6. We modified by hand the resulting “circuits.definitions” file
 1 import sys
 2 from elmer_circuitbuilder import *
 3
 4 def main(argv=None):
 5 output_file = "circuits.definitions"
 6 # ---------------------------------------------------------------------------
 7 c = number_of_circuits(2)
 8 # ---------------------------------------------------------------------------
 9 c[1].ref_node = 1
10 I1 = I("IS1", 1, 2, 100.0)
11 R1 = R("Rcl1", 2, 3, 200.0)
12 FEM_1 = ElmerComponent("Coil1", 3, 4, 1, ["Coil1"])
13 FEM_3 = ElmerComponent("Coil3", 4, 1, 3, ["Coil3"])
14 FEM_1.is3D()
15 FEM_1.stranded(1, 0)
16 FEM_1.isClosed()
17 FEM_3.is3D()
18 FEM_3.stranded(1, 0)
19 FEM_3.isClosed()
20 c[1].components.append([I1, R1, FEM_1, FEM_3])
21 # ---------------------------------------------------------------------------
22 c[2].ref_node = 1
23 I2 = I("IS2", 1, 2, 101.0)
24 R2 = R("Rcl2", 2, 3, 201.0)
25 FEM_2 = ElmerComponent("Coil2", 3, 1, 2, ["Coil2"])
26 FEM_2.is3D()
27 FEM_2.stranded(1, 0)
28 FEM_2.isClosed()
29 c[2].components.append([I2, R2, FEM_2])
30 # ---------------------------------------------------------------------------
31 generate_elmer_circuits(c, output_file)
32 return 0
33
34 if __name__ == "__main__":
35 sys.exit(main() or 0)

---
Cicuits.definitions
circuitBuilder.py
Circuits.definitions
1. 1 $ C.2.variables = 8
2. 2 $ C.2.perm = zeros(C.2.variables)
3. 3 $ C.2.A = zeros(C.2.variables,C.2.variables)
4. 4 $ C.2.B = zeros(C.2.variables,C.2.variables)
5. 5
6. 6 $ C.2.name.1 = "i_IS2"
7. 7 $ C.2.name.2 = "i_Rcl2"
8. 8 $ C.2.name.3 = "i_component(2)"
9. 9 $ C.2.name.4 = "v_IS2"
10. 10 $ C.2.name.5 = "v_Rcl2"
11. 11 $ C.2.name.6 = "v_component(2)"
12. 12 $ C.2.name.7 = "u_2_circuit_2"
13. 13 $ C.2.name.8 = "u_3_circuit_2"
14. 14
15. 15 $ C.2.source.8 = "IS2"
16. 16
17. 17 $ C.2.B(0,0) = -1
18. 18 $ C.2.B(0,1) = 1
19. 19 $ C.2.B(1,1) = -1
20. 20 $ C.2.B(1,2) = 1
21. 21
22. 22 $ C.2.B(2,3) = 1
23. 23 $ C.2.B(2,6) = -1
24. 24 $ C.2.B(3,4) = -1
25. 25 $ C.2.B(3,6) = 1
26. 26 $ C.2.B(3,7) = -1
27. 27 $ C.2.B(4,5) = -1
28. 28 $ C.2.B(4,7) = 1
29. 29
30. 30 $ C.2.B(6,1) = Rcl2
31. 31 $ C.2.B(6,4) = -1
32. 32 $ C.2.B(7,0) = 1
1. 1 $ Circuits = 2
2. 2
3. 3 $ C.1.variables = 11
4. 4 $ C.1.perm = zeros(C.1.variables)
5. 5 $ C.1.A = zeros(C.1.variables,C.1.variables)
6. 6 $ C.1.B = zeros(C.1.variables,C.1.variables)
7. 7
8. 8 $ C.1.name.1 = "i_IS1"
9. 9 $ C.1.name.2 = "i_Rcl1"
10. 10 $ C.1.name.3 = "i_component(1)"
11. 11 $ C.1.name.4 = "i_component(3)"
12. 12 $ C.1.name.5 = "v_IS1"
13. 13 $ C.1.name.6 = "v_Rcl1"
14. 14 $ C.1.name.7 = "v_component(1)"
15. 15 $ C.1.name.8 = "v_component(3)"
16. 16 $ C.1.name.9 = "u_2_circuit_1"
17. 17 $ C.1.name.10 = "u_3_circuit_1"
18. 18 $ C.1.name.11 = "u_4_circuit_1"
19. 19
20. 20 $ C.1.source.11 = "IS1"
21. 21
22. 22 $ C.1.B(0,0) = -1
23. 23 $ C.1.B(0,1) = 1
24. 24 $ C.1.B(1,1) = -1
25. 25 $ C.1.B(1,2) = 1
26. 26 $ C.1.B(2,2) = -1
27. 27 $ C.1.B(2,3) = 1
28. 28
29. 29 $ C.1.B(3,4) = 1
30. 30 $ C.1.B(3,8) = -1
31. 31 $ C.1.B(4,5) = -1
32. 32 $ C.1.B(4,8) = 1
33. 33 $ C.1.B(4,9) = -1
34. 34 $ C.1.B(5,6) = -1
35. 35 $ C.1.B(5,9) = 1
36. 36 $ C.1.B(5,10) = -1
37. 37
38. 38 $ C.1.B(8,1) = Rcl1
39. 39 $ C.1.B(8,5) = -1
40. 40 $ C.1.B(9,7) = -1
41. 41 $ C.1.B(9,10) = 1
42. 42 $ C.1.B(10,0) = 1
1. 1 import sys
2. 2 from elmer_circuitbuilder import *
3. 3
4. 4 def main(argv=None):
5. 5 output_file = "circuits.definitions"
6. 6 # ---------------------------------------------------------------------------
7. 7 c = number_of_circuits(2)
8. 8 # ---------------------------------------------------------------------------
9. 9 c[1].ref_node = 1
10. 10 I1 = I("IS1", 1, 2, 100.0)
11. 11 R1 = R("Rcl1", 2, 3, 200.0)
12. 12 FEM_1 = ElmerComponent("Coil1", 3, 4, 1, ["Coil1"])
13. 13 FEM_3 = ElmerComponent("Coil3", 4, 1, 3, ["Coil3"])
14. 14 FEM_1.is3D()
15. 15 FEM_1.stranded(1, 0)
16. 16 FEM_1.isClosed()
17. 17 FEM_3.is3D()
18. 18 FEM_3.stranded(1, 0)
19. 19 FEM_3.isClosed()
20. 20 c[1].components.append([I1, R1, FEM_1, FEM_3])
21. 21 # ---------------------------------------------------------------------------
22. 22 c[2].ref_node = 1
23. 23 I2 = I("IS2", 1, 2, 101.0)
24. 24 R2 = R("Rcl2", 2, 3, 201.0)
25. 25 FEM_2 = ElmerComponent("Coil2", 3, 1, 2, ["Coil2"])
26. 26 FEM_2.is3D()
27. 27 FEM_2.stranded(1, 0)
28. 28 FEM_2.isClosed()
29. 29 c[2].components.append([I2, R2, FEM_2])
30. 30 # ---------------------------------------------------------------------------
31. 31 generate_elmer_circuits(c, output_file)
32. 32 return 0
33. 33
34. 34 if __name__ == "__main__":
35. 35 sys.exit(main() or 0)

---
Results
Deviation between circuits current:
- The linear case with B = μ0H and σ = cst is working
- The non-linear case B = μ(H)H and σ = cst is working
- The non-linear resistance case B = μ0H and σ(B) is working
The non-linear resistance case B = μ(H)H and σ(B) is working
1. See what else?

---
Information
1. Full code:
2. https://drive.google.com/drive/folders/1JQJGZvbyno8A4lw7-U0Y2NS6hF2eZgdj?usp=sharing
3. Or contact:
4. Frederic Trillaud at ftrillaudp@gmail.com